## Slide 1: SPIRAL 2 - status
Hanna Frånberg Delahaye

## Slide 2: Outline of my talk
GANIL – SPIRAL 2 were are we?
Statistics of operation

## Slide 3: GANIL-SPIRAL2
Particles | H+ | D+ | Ions | 
A/Q | 1 | 2 | 3 | 
Max I (mA) | 5 | 5 | 1 | 
Max energy (MeV/A) | 33 | 20 | 14 | 
Max beam power (kW) | 165 | 200 | 44 | 
July 8th, 2019 Administrative authorization to operate SPIRAL2

## Slide 4: Main commissioning dates and milestones
Milestones
J1: Injector qualification with beam on the D-plate
J3: LINAC RF power qualification
J4: LINAC beam up to the beam dump
J5: Beam in NFS experimental hall
J6: Beam in S3 experimental hall (after the completion of S3)
2021
A/q=2 4He2+ at I=1,3 mA E=20MeV/A
D+ at I=5mA E=20MeV/A (using sbs)
NFS : I=50µA
2022
A/q=3 18O3+ at 60keV ion source.
LHE : 7 MeV/A I= 800µA
LHE – no acceleration : 0,7MeV/A

## Slide 5: Commissioning Time Line
D-plate
LEBT
MEBT
RFQ
LINAC
ECRIS
A/Q=3
1mA
ECRIS
H+, d+
5 mA
2014
P/D source:
first beam
2 mA H+.
December
2018
Diagnostic plate commissioning end
April-November
2020
SBS @ 5 mA H+.
MEBT @1.2 mA 4He2+
SBS* @1.2 mA 4He2+
SC LINAC @ 5 mA H+
16kW H+
July – December
2015
Phoenix V2: first beam 230 µA Ar9+
July.
RFQ: first H+ beam December.
2019
MEBT @5 mA H+.
SBS* @ 0.2 mA H+
SC LINAC @ 0.2 mA H+
33MeV H+
July-December
2021
SC LINAC@1.3 mA 4He2+
SBS @ 5 mA D+
SC LINAC @ 5 mA D+
40 MeV D+
50 µA NFS
July-September
NFS
S3
Beam Dump

## Slide 6: Exploitation

## Slide 7: Operation of LINAC – SPIRAL 2
Increasing operation time for SPIRAL 2 and GANIL.
2019-2020-2021 majority of time for machine learning.
2021 : 750 h for physics of total 3046 h for running.

## Slide 8: 2020 et 2021
Notes: Tuning of the LINAC 32%  21% 730h570
Unused beams 39 %  16 % 920 430h
Physics 9%  24 % 280 h 680h
Technical difficulties 400 890h
The pourcentage of physics was went up due to the availability of deutron beams in NFS
The amount of technical issues went up due to the comissioning of the machine

## Slide 9: Experiments at NFS
Carac 0 |  | 
Carac 1 | Conv mince Li Be | 11 MeV d+
Carac 2 | Conv rotative | 20 MeV d+
E800_20 |  | 20 MeV d+ I=47µA
E811_20 |  | d+ I=10µA 20MeV/A
E807_20 |  | d+ I=10µA 20MeV/A
E799_20 |  | p+ I=300nA 33MeV
LoI – 5 |  | p+ I=20µA 33MeV
LoI – 9 |  | 20 MeV d+ I=47µA

## Slide 10: Operation
2020
The LINAC proton acceleration at 16 kW was accomplished.
Full operation 24h/24 7d/7 was put in place.
2021
3 runs:
Deuterons 20 MeV/A
  Tests :
    ACCT/DCCT
    Bunch selector
      Optimisation of tuning with different frequencies
    Modification of the scrapper
    BPM (noise reductions,
Experiments with neutron converter at NFS
  Characterisation of converters

## Slide 11: Technical issues 2020 and 2021
Due to the operation of deuteron beams and higher power achieved in 2021 the technical issues also increased.
Some of the necessary modifications were:
  the beam bunch selector equipment. A new design was made and installed for the run 2022
  Spare equipment's for the power supplies for the same has been foreseen.
  A RF tube for one of the cavity underwent serious damages and was exchanged.
  The deuteron source had isolation difficulties on the RF tube.
  A modification of the filters for the RF tubes for the RFQ was obligatory .
Various modifications of the beam diagnostics and monitoring were performed while gaining knowledge of their behaviour with beam.
New algorithms for tuning of the cavities - Control systems
Changes in the alarm system for the different equipment.
  Faster intervention time 24h/7

## Slide 12: High lights

## Slide 13: Technical talks this week :
Monday
  Session 4: SPIRAL 1 beams
Wednesday:
  Session 3: CSS renovation sessions
Thursday:
  Session 3: Inter-facility developments
  Session 4: SPIRAL2 : Accelerator Perspective
Friday
  Session 1: DESIR
I wish you a very nice conference and plenty of discussions.