## Slide 1: SPIRAL1 Flash talk & discussions

## Slide 2
SPIRAL1 : Machine status
1+
N+
CF13
CF81
CF11
CF41
CF31
TISS
Machine is now reliable, and efficiencies are in accordance with initial objectives
Phase | Objectives Initial | 2021 47K10+ 7MeV/A
Production (Ar) | 10% | <20%
1+ to N+ transport | 80% | >80%
Charge Breeding | 5-10% | 8%
Extraction N+ | 50% | 80%
CIME | 20% | <20%

## Slide 3
SPIRAL1 : Production
Nanogan3
FEBIAD
SIS
Fusion-evaporation
Under development
Available TISS - Fragmentation
Discussions for future developments :
Increase production (target, prim. Beam, …)
Purity (prim. beam, molecule, Laser, …)
Variety (fusion evaporation, new TISS, …)
to be checked

## Slide 4
ISOLDE ions beams produced with Lasers
SPIRAL1 Target fragmentation process up to Nb
Reference :
« Ion beam production and study of radioactive isotopes with the laser ion source at Isolde »
Valentin Fedosseev et al – 2017 J. Phys. G : Nucl.Part. Phys. 44 084006
SPIRAL1 : Laser ion source
Ionization schemes existing :
Publication
Development of new ionization schemes have to be done if unknown
    Could be done on GISELE tests bench according to source availability
Discussion with N. Lecesne

## Slide 5
SPIRAL1 : Laser ion source
Technical installation :
Laser devices, equipements and infrastructure requirements are well known (GISELE, S3)
Define the best location
Safety authorization :
Some Laser installations are already studied at GANIL (GISELE, S3)
Technical solutions are already developed for fire protection and nuclear ventilation constraint.
Interne authorization should be ok, but have to be check with a more precise project
Cost :
Laser equipement : 500k€
Laser room and infrastructure : 180k€ (S3)
Human ressource :
1 reseach engineer + 1 PhD to adapt TISS, install Laser and develop ionization schemes
Discussion with N. Lecesne

## Slide 6
SPIRAL1 : Laser ion source
Laser room
  Orange : 0 level
  Bleu : Underground
Laser room
ECS
Laser system
D1P